## Slide 1: Arduino Workshop #3
Reading Analog Sensors
Notes: 24 – Arduino Uno
24 - Small bread board
24 – Jumper wire sets
24 - 10 kΩ potentiometer
48 – 10 kΩ resistor
72 – 220 Ω resistor
24 – USB cables
24 – photoresistors
24 - TMP36 temperature sensor (or any other 5 V analog sensor)
24 – 5mm common-cathode RGB LED

## Slide 2: Why we still need analog in a “digital world”?
Observable features are analog
  they can assume any number of potential states
    Color of sunlight
    Temperature
    Concentration of contaminants in the air
So we need a way to distinguish between analog and digital inputs and convert between the two

## Slide 3: Analog to digital converter
Suppose you want to measure the brightness of the room (measured in lux - it could be any decimal from 0 to ∞)
Pitch black - output 0 volts
Completely saturated - outputs 5 volts
Half saturated - outputs 4.5 volts
⅓ saturated - outputs 1.6666 volts
etc.
You need to use the analog to digital converter (ADC) built into the Arduino to read this value

## Slide 4: But what is a ADC doing?
In the Arduino
  10-bit ADC
    This means that the ADC can subdivide (or quantize) an analog signal into 210 different values
      210 = 1024
    So from the reference voltage (5 v)
      2.5 v is mapped to 512 (½ of 1024)
      1.25 v is mapped to 256 (¼ of 1024)
      etc.

## Slide 5: Visual of what’s happening
Here is a 2 bit ADC, it has 2 bits of resolution and therefore 4 total logic levels (22 = 4)
The higher the resolution the more “steps” in the digitized signal (remember the Arduino has 10 bit resolution… so 1024 steps)

## Slide 6: Reading analog signals
Let's start with a potentiometer
  Pot for short
  Used in
    car stereos
    Thermostats
    speakers
    Etc.
  3 pins
    Outer is grounded (symmetrical so it doesn't matter which side)
    Other side pin is connected to high (5 v)
    Inner pin is connected to low (0 v)
  As you turn the knob you are changing the resistance and thus the output voltage (by ohm's law) to any value between 0 v and 5 v

## Slide 7: Lets wire up a circuit

## Slide 8: Write the code to see the readings

## Slide 9: Notice the new functions
analogRead()
  This function reads the value of the analog pin connected to the Arduino
Serial.println()
  This function prints to the Arduino IDE serial monitor
serial.begin()
  In the setup section
  Takes an argument that specifies the communication rate (baud rate)
    Faster baud = more data in less time
      Can induce transmission error
    9600 is common value (and will be the standard we use)

## Slide 10: What you should see
The TX LED on the Arduino should be blinking every 500 ms
  This indicated the Arduino is transmitting data
After launching the serial monitor you should see a window w/ numbers streaming by
  Turning the dial the numbers should go up and down (corresponding to the position of the potentiometer)
    One way goes toward 0
    The other towards 1023
  If you are getting “funky data” you need to ensure the baud rate is correctly set on the monitor
Serial Monitor

## Slide 11: Use an analog sensor to sense temperature

## Slide 12: Wire it up

## Slide 13: Before we can begin
We need cut offs
  Using the same concepts as before we can find
    Launch the sketch from before and see what “room temp” corresponds to
      When writing this 200 C was about 143 (these will be different for you)
    Do a bit of math
      Temp (0 C) x 10 = voltage ( mV ) - 500
      From here we can see that if we want to set upper and lower points all we need to do is solve for the voltage then we can convert that to use in the Arduino
      For my 200 C room
        20 * 10 = x -500
          X = 700 mV
        700 mV / (5 V) = Y / 1024
          Y = 143.36 (which is 143)
      You need to do this for two other temps (2 degrees higher and 2 degrees lower)
        These will be the temp that changes the light

## Slide 14: Try it yourself first
Goal to get to
  Try to write a code that
    When the temperature is with in “room temp” ± 2 0C the led is Green
    If the temp is lower than that the LED is Blue
    If the temp is higher than that the LED is Red
  You don't need any new concepts
    This is simply building on the concepts from session 1 & 2 (plus the concepts from today)
In about 10 minutes we will go over how one possible code looks

## Slide 15: One possible code

## Slide 16: make your own analog sensor

## Slide 17: Thanks Physics
Not all resistors are constant value of resistance
  Conductivity changes resistance when stressed
    Force sensors
    Flex sensors
  Some semiconductors change resistance due to light
    Photoresistors
  Metals change resistance due to temperature
    Thermistors
We can take advantage of this with a voltage divider (so we can measure the change in resistance)

## Slide 18: What is a resistive voltage divider?
Uses two resistors to output a voltage that is some fraction of the input voltage
  Output is directly related to the value of the 2 resistors
    If one resistor is variable you can monitor the ΔV and calculate the ΔR

## Slide 19: Add in a photoresistor
A photoresistor
  Changes resistance based on the amount of light it receives
    Darker is higher resistance
Whether you replace R1 or R2 and the value you choose for the fixed resistor will affect your reading
  Scale and Precision
Experiment and look at your serial monitor
Once you have a idea
  Find values of a “dark” room
  Find values of a “light” room

## Slide 20: Start coding
recall
  analogWrite()
    Sets the brightness of the LED
    Accepts values between 0 and 255
New function
  map()
    Output = map(value, fromLow, fromHigh, toLow, toHigh)
      Value - the information you start with
        Most recent reading from analog input
      fromLow and fromHigh
        Input boundaries
          Min and Max brightness
      toLow and toHigh
          Values you want to map to
            255 and 0 (swapped to turn off the light when bright)

## Slide 21: New function
map()
Output = map(value, fromLow, fromHigh, toLow, toHigh)
  Value - the information you start with
    Most recent reading from analog input
  fromLow and fromHigh
    Input boundaries
      Min and Max brightness
  toLow and toHigh
      Values you want to map to
        255 and 0 (swapped to turn off the light when bright)
constrain()
constrain(value, min, max)
  Constrains the value given between 2 values
    If the photo resistor measured to high you would pass below 0 (its inverted to turn off in light)

## Slide 22: Add the Photoresistor
Insert the Photo Diode into Analog In 0

## Slide 23: The code